NivuFlow 650

Flow rate measurement for clear to slightly polluted 
media in pipes and various part filled and full

channel profiles.

Detection of average flow velocities in up to 4 measurement

paths based on the transit time difference principle.

Detection of water surface level and individual

flow velocities.

Flow measurement transmitter with integrated numeric

discharge models to detect the average flow velocity

from up to 4 individual flow velocities (acoustic paths).

Connecting options and calculation functions for

up to 4 paths to determine the accurate flow profile
distribution in channels or part filled channel shapes.

Calculation of the real flow profile by integrating

all measured path velocities covering the wetted cross-

sectional area.

Flow rate calculation from average flow velocity, filling

level and channel shape considering the medium temperature,

channel shape, channel dimensions and degree of partial

filling based on internal numeric discharge models.

Storage, graphic representation and transmission of

all relevant measurement data.

Detection of water surface level using ultrasound from

bottom up; via pressure measurement cell, ultrasound

from top down or separate level measurement.

Up to three level measurement methods can be combined

for optimum adjustment of the measurement to high

measurement dynamics and difficult hydraulic

applications as well as for redundant detection under

critical measurement conditions.

Metal-encapsulated compact enclosure with easy accessible

front-side terminal cage clamps for quick installation
and mounting.

Large full colour TFT graphic daylight display featuring

240 x 320 pixel and 65536 colours.

Optimum display clarity even in direct sunlight thanks to

1:400 contrast ratio and up to 80° possible deviation

from observation plane in any direction.

Modern intuitive one-hand operation using rotary

pushbutton together with high-resolution

graphic colour display.

Programming with flat hierarchical structure, supported

by colours and graphic elements, visual true-to-scale

representation even of complex canal shapes and sensor 
positions in order to avoid errors during commissioning.

Intelligent error and sensor diagnostics.

Integrated recorder function with min. and max. memory.

Storage of all path velocities, levels, average flow velocities,

flow rates and medium temperature in internal high capacity

memory.

Programming data and all saved readings as well errors

as can be copied to standard USB stick via front-side

USB interface.

HART interface for direct connection of compatible

sensors.

Connection by using RS232/485 interface.

Worldwide interface standard via TCP/IP/Ethernet

Online access using Internet browser without the need to

install additional software.

Integration of the transmitter into higher systems

via ModBus TCP/RTU

Operating voltage: 	85 – 240 V AC

9 – 36 V DC (optional)

Construction:	DIN rail

field enclosure (optional)

Enclosure material:	profile aluminium (DIN rail)
	plastic (field enclosure)

Protection:	IP 20 (DIN rail)
	IP 68 (field enclosure)

Display:	full colour graphic TFT daylight display

240 x 320 px, 65536 colours

contrast min. 1:400

Programming:	dialog mode using rotary pushbutton

and 2 function keys

Versions: 	NF6 5T2 (up to 2 paths)

NF6 5T4 (up to 4 paths)

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Flow-optimised hemisphere sensor for flow velocity

measurement for mounting on abutments.

Three-dimensional alignment options of sound beam.

Detection of average flow velocity along the

measurement layer through sensor-integrated ultrasonic

converter with bundled directivity.

Measurement uncertainty during detection of average

path velocities higher than 0.125%.

Underwater plug connection for easy installation on site

and wet installation of converters.

Measurement range:	-10 m/s to +10 m/s

Path length:	1 m to 40 m

Transm. frequency:	1 MHz

Materials:	stainless steel 1.4301, CFK, Viton,
PUR; POM, Neoprene

Protection:	IP 68

Pressure resistance:	up to 12 m H2O

Cable length:	10 m (option: 15/20/30/50/100 m)

Version:	NOS V30 BS

Deliver and install ready to use as pairs

Type:............................

Make:.....................

Quantity:  1 Pair	UP: ..................

TP: ....................

Flow-optimised hemisphere sensor for flow velocity

measurement for mounting on vertical and sloped

walls.

Two-dimensional alignment options for sound beam.

Detection of average flow velocity along the

measurement layer through sensor-integrated ultrasonic

converter with bundled directivity.

Measurement uncertainty during detection of average

path velocities higher than 0.125%.

Measurement range:	-10 m/s to +10 m/s

Path length:	1 m to 10 m

Transm. frequency:	1 MHz

Materials:	stainless steel 1.4571; CFK

Protection:	IP 68

Pressure resistance:	up to 160 m H2O

Cable length:	10 m (Option:15/20/30/50/100 m)

Version:	NIS V280 KS

Deliver and install ready to use as pairs

Type:............................

Make:.....................

Quantity:  1 Pair	UP: ..................

TP: ....................

Flow velocity rod sensor for mounting on

vertical abutments.

Two-dimensional alignment options for sound beam.

Detection of average flow velocity along the

measurement layer through sensor-integrated ultrasonic

converter with bundled directivity.

Measurement uncertainty during detection of average

path velocities higher than 0.125%.

Measurement range:	-5 m/s to +5 m/s

Path length:	1 m to 20 m

Transm. frequency:	1 MHz

Materials:	stainless steel 1.4301, CFK, Viton,

Protection:	IP 68

Pressure resistance:	up to 50m H2O

Pipe length:	500 mm, extendable in

steps of 1000 mm

Cable length:	10 m (option:15/20/30/50/100m)

Version:	NOS V200 5

Deliver and install ready to use as pairs

Type:............................

Make:.....................

Quantity:  1 Pair	UP: ..................

TP: ....................

Flow velocity rod sensor for mounting on

vertical abutments.

Two-dimensional alignment options for sound beam.

Detection of average flow velocity along the

measurement layer through sensor-integrated ultrasonic

converter with bundled directivity.

Measurement uncertainty during detection of average

path velocities higher than 0.125%.

Measurement range:	-5 m/s to +5 m/s

Path length:	1 m to 40 m

Transm. frequency:	1 MHz

Materials:	stainless steel 1.4301, CFK, Viton,

Protection:	IP 68

Pressure resistance:	up to 40m H2O

Pipe length:	500 mm, extendable in

steps of 1000 mm

Cable length:	10 m (option:15/20/30/50/100m)

Version:	NOS V200 5

Deliver and install ready to use as pairs

Type:............................

Make:.....................

Quantity:  1 Pair	UP: ..................

TP: ....................

Flow velocity rod sensor for mounting on

vertical abutments.

Two-dimensional alignment options for sound beam.

Detection of average flow velocity along the

measurement layer through sensor-integrated ultrasonic

converter with bundled directivity.

Measurement uncertainty during detection of average

path velocities higher than 0.125%.

Measurement range:	-5 m/s to +5 m/s

Path length:	5 m to 100 m

Transm. frequency:	200 KHz

Materials:	stainless steel 1.4301, CFK, Viton,

Protection:	IP 68

Pressure resistance:	up to 40m H2O

Pipe length:	500 mm, extendable in

steps of 1000 mm

Cable length:	10 m (option:15/20/30/50/100m)

Version:	NOS V200 5

Deliver and install ready to use as pairs

Type:............................

Make:.....................

Quantity:  1 Pair	UP: ..................

TP: ....................

Extension tube with fine thread, suitable for

flow velocity rod sensors Type NOS-V2005,

NOS-V3005 and NOS-V4005

Material:	stainless steel 1.4571

Length:	1000 mm

Version:	NOZ0 ROHR VE1

Deliver and install incl. all required corrosion-proof

mounting components

Type:............................

Make:.....................

Quantity:  1 Pair	UP: ..................

TP: ....................

Ultrasonic level meter consisting of ultrasonic

sensor with temperature sensor for compensation

of ultrasound transit time and sensor-integrated free

programmable evaluation electronic.

Encapsulated, permanently immersible sensor in
corrosion-proof enclosure featuring high chemical

resistance.

Suitable for measurement of liquids and pasty media

Meas. ranges:	0.125 up to 3 m or

0.3 up to 6 m or

0.3 – 10 m

Meas. uncertainty:	0.25%

(distance sensor-surface)

Memory:	Flash

Calibration:	via HART

Enclosure:	Valox 357

Temperature range:	-40 to max. +80 °C

Protection:	IP 68

Flood detection	using SUB-sleeve (option)

Output:	4 - 20 mA / HART

Cable length:	10 m; (option: 20/30 m)

extendable up to 1000 m

Versions:	NMI0 03
	NMI0 06

NMI0 10

Deliver, install ready to use and calibrate

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Hydrostatic level measurement as cable sensor,

with ceramics measurement cell and integrated

evaluation electronic incl. overvoltage protection, suitable

for measurement of slight to heavily polluted media.

Cable-integrated strain relief and venting.

Power supply:	12 to 36 V DC

Meas. ranges:	2; 4; 6; 10 m H2O

Cable length:	20 m

Cable material:	Polyurethane

Measurement cell:	capacitive with ceramics membrane

and Viton gasket

Temperature:	-10 to max. +70°C

Enclosure material: 	stainless steel 1.4571

Output signal:	4 - 20 mA

Meas. uncertainty:	± 0.25%

Long-term stability:	± 0.1% FSO/year

Zero point:	± 0.1% FSO/year

Protection:	IP68

Version:	HSB0 NBP

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Corrosion-proof straining clamp for variable

straining of cables with outside diameters

from 7.5 to 10.5mm.

Material:	1.4571

Version:	AKL 1

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Junction box with pressure compensation, suitable for

connection and direct extension of cable sensors.

Version:	BPG 1

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Power lines overvoltage protection

High-performance overvoltage limiter

for 230 V AC power inputs with 16 A current,

according to German DWA A-M 261 suitable as

overvoltage protection for wastewater treatment plants

Overvoltage protection with very high leakage capacity.

Varistor self-control and independent disconnection

from mains in case of  exceeding leakage currents.

Visual indication of operation and malfunction

Nominal leakage

current wire-ground:	20 KA

Maximum

operating voltage:	300 V AC

Protection rating:	1.1 kV wire-ground

Installation:	35 mm DIN rail

Enclosure:	Polycarbonate

Model:	EnerPro 220 Tr/20

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Initial commissioning of the completely installed

measurement system on site incl. installed and

connected sensors carried out by manufacturer.

Verification of hydraulic compatibility of installation

place, correct installation of sensors and transmitter.

Verification of sensor signals and – if possible on site

and without diving works or repositioning of sensors -

adjustment of the sensors used.

Handover of parameter lists containing relevant settings

of the measurement system as well as a commissioning

record.

Quantity:  1 Flat Rate	UP: xxxxxxxxxx

TP: ....................