CS2 Sensor

Flow rate measurement in part filled and full

pipes and any channel profile with large dimensions

Detection of water surface level as well as of up to 16

spatially allocated flow velocities

Flow calculator for investigation and storage of

flow rates calculated from flow velocity and

water level

Detection of spatially allocated flow velocity

profiles using the correlation method and digital

pattern detection

Calculation of real 3D flow profiles through integration

of all 16 measured spatial velocities across the

wetted cross-sectional area

Investigation of water surface level using two

redundant ultrasonic sensors from bottom up; using  the

sensor-integrated pressure measurement cell or separate

level measurement

Temperature compensation of all measurement values

Indication of readings on large back-lit graphic display

Graphic representation of velocity distribution and

measured individual velocities

Worldwide interface standard via TCP/IP/Ethernet.

Online access via Internet browser without the need to

install additional Software incl. options for direct setting

of parameters, operation and data transmission.

Logging function with 90-day trend graph

Clear text programming in dialog mode via

front-side alphanumeric keypad with membrane cover

Storage of all individual velocities, fill level, average

flow velocity, flow rate and medium temperature on

plug-in flash card

Power supply: 	100 – 240 V AC

9 - 36 V DC (option)

Construction:	wall mount enclosure

Protection:	IP 65

Ex approval:	Zone 1 (option)

Display:	back-lit graphic display, 128 x 128 pixel

Inputs:	1 x 4-20 mA, galvanically isolated

Outputs:	2 x 4-20 mA, galvanically isolated

2 x relays (SPDT)

Memory capacity:	up to 128 MB auf CompactFlash(

Communication:	Ethernet, analog or ISDN modem

GPRS (please specify), 
ModBus TCP, integrated web server

Model: 	OCP-S4W0

incl. NivuDat readout software and NivuSoft evaluation 
software for Windows 2000/XP/7

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Flow-optimised flow velocity sensor for

installation on the channel bottom, channel side or for

floating installation

Detection of up to 32 spatially allocated flow

velocities using 2 sensor-integrated ultrasonic

sensors aligned according to vectors

Measurement range:	- 100 cm/s to 600 cm/s

Meas. uncertainty:	1 % of measurement range

Materials:	stainless steel 1.4571; PPO GF30

PA6 GF30, CFK, PU

Protection:	IP 68

Ex approval:	Zone 1 (option)

Cable length:	10 m (option: 15/20/30/50/100 m)

extendable up to 250 m

Cable protection:	corrugated stainless steel pipe for

mechanic protection and to protect

against rat bites (option)

Model:	CS2-V200

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Flow-optimised flow velocity sensor for

installation on the channel bottom, channel side or for

floating installation

Detection of up to 32 spatially allocated flow

velocities using 2 sensor-integrated ultrasonic

sensors aligned according to vectors

Flow level detection using two redundant ultrasonic

sensors

Measurement range

flow velocity:	- 100 cm/s to 600 cm/s

Water-ultrasound:	12 – 400 cm

Meas. uncertainties

flow velocity:	1 % of measurement range

Water-ultrasound:	better than 2 mm

Materials:	stainless steel 1.4571; PPO GF30

PA6 GF30, CFK, PU

Protection:	IP 68

Ex approval:	Zone 1 (option)

Cable length:	10 m (option: 15/20/30/50/100 m)

extendable up to 250 m

Cable protection:	corrugated stainless steel pipe for

mechanic protection and to protect

against rat bites (option)

Model:	CS2-V2H1

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Flow-optimised flow velocity sensor for

installation on the channel bottom, channel side or for

floating installation

Detection of up to 32 spatially allocated flow

velocities using 2 sensor-integrated ultrasonic

sensors aligned according to vectors

Flow level detection using sensor-integrated

pressure measurement cell

Measurement range

flow velocity:	- 100 cm/s to 600 cm/s

Pressure cell:	0 – 350 cm

Meas. uncertainties

flow velocity:	1 % of measurement range

Pressure cell:	max. 0.75 % zero point drift/MB

max. 0.5 % of final value

Materials:	stainless steel 1.4571; PPO GF30

PA6 GF30, CFK, PU

Protection:	IP 68

Ex approval:	Zone 1 (option)

Cable length:	10 m (option: 15/20/30 m)

via pressure compensation element 
extendable to up to 250 m

Cable protection:	corrugated stainless steel pipe for

mechanic protection and to protect

against rat bites (option)

Model:	CS2-V2D0

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Flow-optimised flow velocity sensor with additional 
pressure measurement cell for installation on the channel

bottom, channel side or for floating installation

Detection of up to 32 spatially allocated flow

velocities using 2 sensor-integrated ultrasonic

sensors aligned according to vectors

Flow level detection using two redundant ultrasonic

sensors as well as an additional sensor-integrated

pressure measurement cell

Measurement range

flow velocity:	- 100 cm/s to 600 cm/s

Water-ultrasound:	12 – 400 cm

Pressure cell:	0 – 350 cm

Meas. uncertainties

flow velocity:	1 % of measurement range

Water-ultrasound:	better than 2 mm

Pressure cell:	max. 0.75 % zero point drift/MB

max. 0.5 % of final value

Materials:	stainless steel 1.4571; PPO GF30

PA6 GF30, CFK, PU

Protection:	IP 68

Ex approval:	Zone 1 (option)

Cable length:	10 m (Option: 15/20/30 m)

via pressure compensation element 
extendable to up to 250 m

Cable protection:	corrugated stainless steel pipe for

mechanic protection and to protect

against rat bites (option)

Model:	CS2-V2U1

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Sensor line overvoltage protection

Lightning and overvoltage protection for potential-free

data lines

High-performance overvoltage limiter with

coarse and fine protection, with minimum internal

resistance, particularly adjusted to LUS and POA sensors

Internal self-control using failsafe diodes

Maintenance-free due to high electronic

Nominal leakage

surge current

(8/20 µs):	20 kA

Max. operation

voltage:	12 V DC/24 V DC

Series resistance:	0.3 Ohm

Installation:	35 mm DIN rail

Enclosure:	plastic

Ex approval:	Zone 1 (option)

Models:	1x DataPro 2x1-12V/12V-11µH

1x SonicPro 3x1-24/24V

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Analog output overvoltage protection

Lightning and overvoltage protection for potential-free

data lines

High-performance overvoltage limiter with

coarse and fine protection for symmetric or

galvanically isolated data line inputs and

outputs as well as for 2-wire systems

Suitable for transmission frequencies up to 600 kHz

and 0.5 A operating current

Internal self-control using failsafe diodes

which short-out data lines in case of error.

Maintenance-free due to high electronic

overdimensioning

Nominal leakage

surge current

(8/20 µs):	20 kA

Maximum

operating voltage:	28 V DC / 20 V AC

Protection rating:	36 V wire-ground

Installation:	35mm DIN rail

Enclosure:	plastic

Ex approval:	Zone 1 (option)

Model:	DataPro 2x1-24/24V

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Power lines overvoltage protection

High-performance overvoltage limiter according to ATV H 261

for 230 V AC power inputs with 16 A current.

Overvoltage protection with very high leakage capacity.

Varistor self-control and independent disconnection

from mains in case of  exceeding leakage currents.

Visual indication of operation and malfunction

Nominal leakage

current wire-ground:	20 KA

Maximum

operating voltage:	300 V AC

Protection rating:	1.1 kV wire-ground

Installation:	35 mm DIN rail

Enclosure:	Polycarbonate

Model:	EnerPro 220 Tr/20

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Accessories

Memory card for mobile data transport

Industry standard with extended temperature range,

suitable for OCM Pro, PCM Pro, PCM 4, NivuSonic

and NivuChannel

Suitable for storage of all individual velocities,

average velocity, level, flow rate,

temperature as well as additional inputs

Memory capacity:	128 MB

Temperature range:	-40 °C to 85 °C

Type:	CompactFlash( card 128 MB
Deliver

Type:............................

Make:.....................

Quantity:  2 Pcs.	UP: ..................

TP: ....................

Readout device for CompactFlash( card,

connection via USB interface

Deliver

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Pressure compensation element

for connection or extension of active sensors

Types V1U, V1D, V2U and V2D

Consisting of metal connection box incl. clamps,

pressure compensation plug and coupling as well as

large air filter with visible indication of

absorption of air humidity.

Enclosure:	Aluminium die cast

Protection:	IP 65 (enclosure)

IP 40 (filter)

Type:	ZUB0 DAE

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Initial commissioning of measurement by manufacturer

of the measurement system

Verification of hydraulic suitability of the measurement

place, the correct sensor installation as well as the

transmitter installation

Setup and verification of the measurement

according to VDE/VDI 2640

Handover of parameter lists containing the settings

implemented on the measurement systems as well as

a commissioning report

Quantity:  1 Flat rate	UP: xxxxxxxxxx

TP: ....................